## Slide 3: TCP Header
Source: https://de.wikipedia.org/wiki/Transmission_Control_Protocol#Aufbau_des_TCP-Headers

## Slide 4
FEC - Forward Error Correction
FED - Forward Error Detection
MAC - Medium Access Channel
IP - Internet Protocol
TCP - Transmission Control Protocol
Payload
e.g. 802.3an 10 Gigabit Ethernet
payload (1723 bits), redundancy (2048 bits)
e.g. CRC-32
payload (<see below> bit), redundancy (32 bit)
(<64 bytes: 8-bit CRC; <16K bytes: 16-bit CRC; <512M bytes: 32-bit CRC)
e.g. Ethernet:
preamble (8 byte), destination address (6 byte), source address (6 byte), length, payload (0 - 1500 byte), pad (0 - 46 byte), checksum (4 byte)
e.g. IPv4:
Version (4 bit), IHL - IP header length (4 bit), Total length in bytes (16 bit), …,
Protocol (8 bit), …, source address (32 bit), destination address (32 bit),
payload ((2^16 - sizeof(header)) byte)
Physical layer
Data link layer
Network layer
Transport layer
Applicat. layer
e.g. TCP:
source port (16 bit), destination port (16 bit),
sequence number (32 bit), acknowledgement number (32 bit),
e.g. VIB (Very Important Bits)

## Slide 5
Transport layer
Devices: Transport Gateway
TCP packet
TCP packet
Appl. Port X
Appl. Port Y
Appl. Port Z
Appl. Port X
Appl. Port Y
Appl. Port Z
TCP implementation
(Tahoe, Reno, Vegas, Cubic, ...)
Forward Packets to correct ports
Tahoe: Slow start until threshold; additive increase until packet loss; reset CW
Reno: Listen to 3rd dup. Ack; resend missing packet; divide CW and threshold in half
Vegas: use dynamic RTTs to manage outgoing packets
Cubic: Use cubic equation to calculate CW

## Slide 6
Devices: Router
IP packet
IP packet
Network layer
For my Database?
yes
no
Algorithms
Distance-vector routing algorithm
(e.g. bellman-ford algorithm)
Link-state routing algorithm
(e.g. dijkstra algorithm)
is basis of
For my local network?
For me?
Forwarding table
(longest prefix matching)
Routing table
generates
yes
TCP packet
TCP packet
no
yes
no
DHCP
(Dynamic Host
Configuration Protocol)
ask for IP address
( )

## Slide 7
Devices: Router
IP packet
IP packet
Algorithms
Distance-vector routing algorithm
(e.g. bellman-ford algorithm)
Link-state routing algorithm
(e.g. dijkstra algorithm)
is basis of
Forwarding table
(longest prefix matching)
Routing table
generates
TCP packet
TCP packet
For me?
DHCP, ggf. NAT
yes
no
for my local network
not for my local network
Local IP address space
Global IP address space
Network layer

## Slide 8
Success / failure
MAC Sublayer
Devices: Switch, Bridge
ARP
(Address Resolution Protocol)
Step 1:
Ask for MAC
for given IP
Step 3: Send Packet to destination MAC
Is ARP response?
no
yes, Step 2: Get requested destination MAC
MAC algorithm
(ALOHA, CSMA, …)
IP packet
IP packet
MAC frame
MAC frame

## Slide 9
Framing
Forward error
correction
Error
detection
Backward
error
correction
Byte stuffing
Character counting
Bit stuffing
Code violations
Odd / even pairity
CRC (Cyclic Redundancy Check)
e.g. 32-bit CRC
BCH codes
e.g. Hamming7,4
Convolutional code
encode using a state machine
Viterbi algorithm
decoding conv. codes
Turbo codes
e.g. multiple conv. codes
Interleaving
ARQ
(Automatic Repeat reQuest protocol)
Devices: Switch, Bridge
Data link layer
Success / failure
MAC frame
Bitstream
Bitstream
MAC frame
Reed-Solomon codes
e.g. manchester encoding
_|-|_|-|__-|_|-|_|---|
Sliding window
systematic / non-systematic block codes
0011 | 1111 1100 | 0000
Code books
(Hamming distance)
decoded by
special case

## Slide 10
Physical layer
Channel
Physical sender
Physical receiver
Attenuation
Signal bandwidth
Channel bandwidth
Distortion
Noise
SNR
Sampling
Data rate bit/s
Symbol rate (baud rate) baud/s
Nyquist limit
Max. Rate without bit errors < 2H*log2(V)
H: Channel bandwidth
V: Number of unique Symbols
Shannon Limit
Max. Rate without bit errors < H*log2(1+ S/N)
H: Channel bandwidth
S: Signal power
R: Noise power
Baseband
Broadband
BER
Constellation Diagram
Channel coefficient
Data rate delay product
Data in channel = rate * τ
Clock drift
Shannon capacity
Devices: Hub, Repeater
Bitstream
Bitstream
Buffer

## Slide 11: Additional information - Forwarding / Routing Table
Forwarding Table | 
Address prefix | Outgoing link
222.123.32.0/24 | 1
222.123.0.0/16 | 2
Routing Table |  |  | Cost
Destination |  | 222.123.0.0/16 | 222.123.32.0/24
Outgoing link | 1 | 12 | 2
 | 2 | 3 | 7

## Slide 12: Additional information - ARP
ARP, Tannebaum, Page 468

## Slide 13
Packet
Packet
Success / failure
Static multiplexing
Collision-based protocol
Collision-free protocol
Limited contention protocols
Packet
Packet
Devices: Switch, Bridge
Time slots
Frequency slots
ALOHA
Slotted ALOHA
CSMA
(Carrier Sense
Multiple Access)
1-persistent CSMA
Non-persistent CSMA
p-persistent CSMA
CSMA/CD
(… Collision Detection)
Static TDMA
Static FDMA
Bit-map protocol
Adaptive tree walk
(adjust number of slots
based on a tree structure)
Static multiplexing
MAC Sublayer
Collision-based protocol
Collision-free protocol
Limited contention protocols
Additional information -
MAC Sublayer

## Slide 14: Weg - Zeit - Diagramm
Weg
Zeit
packet time = packet size / data rate
ack packet time = ack packet size / data rate
delay
delay
data rate - delay - product:
max. number of bits stored inside channel
RTT
RTD